## Slide 1: TCP/IP socket-based communication for SystemVerilog simulation
Victor Besyakov
BTA Design Services, IC Verimeter
May 16, 2018
Boston

## Slide 2: Agenda
Introduction
“TCP/IP Shunt” Library
User Application Example
Summary
Notes: After a short introduction, we will have a brief Socket interface and DPI overview, then we’ll present "TCP/IP Shunt library" as an example of the Socket interface and DPI integration. And finally, we will show how to build user defined handshake by using Shunt structures and methods.

## Slide 3: Introduction
Multi Chip, Multi Environment Simulation
Hardware/Software Co-Simulation
Software Driven Hardware Verification Test Environment
IP evaluation over the Internet
Statistic driven tests (Regression Management)
TCP Socket ,What is it good for?
SV Simulation
TCP
Virtual CPU(QEMU)
SV Simulation
Reference Model (Analog)
Remote IP(VIP)
Regression Manager
SV Simulation
TCP
SV Simulation
TCP
SV Simulation
TCP
SV Simulation
TCP
Notes: Traditionally, data exchange with the world outside the SV simulation space is done trough DPI directly. However, for some RTL simulation, TCI/IP socket communication can offer substantial benefits. The vast majority of those simulations are related to the standalone System Verilog simulations and standalone external applications. For example:
SV to SV When we need to ensure chipset compatibility we can make Chipset co-simulation.
External application to SV: it can be Software-hardware verification. When standalone CPU debugger is connected to the standalone SV simulation,
External application to SV: it can be Analog/mixed-signal co-simulation. When standalone external analog (Matlab or C/System model is connected to SV simulation.
SV to SV distributed simulation for remote IP evaluation over the internet.
External application to SV: to connect Stand Alone coverage DataBase application to several SV simulation In order to create reactive TB.

## Slide 4: Introduction
An idea to establish communication with RTL simulations by using TCP has been around for nearly as long as Verilog
“Our solution implements the software components as separate programs that use Unix interprocess communication (IPC) mechanisms to interact with the hardware simulation” D. Becker, R.K. Singh, and S.G. Tell, “An Engineering Environment for Hardware Software CO-Simulation,” DAC 1992
“For debugging purposes, a simple C++ code opens an Ethernet socket and exchanges Ethernet packets between the socket and the verification environment (over DPI).” A. Fiergolski “Simulation environment based on the Universal Verification Methodology” 2017 JINST 12 C0100
History
Smart Regression Manager
Regression Manager(C++)
Simulation test 3
Simulation test 2
Simulation test 4
Simulation test 1
Simulation test N
TCP/
IP
Notes: An idea to establish communication between RTL simulations by using TCP is not a new one.
So, several years ago, when I start development of an application that manages regression DB, gathers statistics and errors from different test runs and making an on-the-fly decision to continue a particular test or to finish it and run a new one.
I was pretty sure that I can easily find examples, tutorials or even freeware that related to the TCP/IP and DPI integration.

## Slide 5: Introduction
TCP
What is the Best C/C++ Network Library?
https://stackoverflow.com/questions/118945/best-c-c-network-library
“Boost.Asio is really good.”
“Asio is also available as a stand-alone library.”
“ACE is also good, a bit more mature and has a couple of books to support it.”
Tutorial:
https://beej.us/guide/bgipc “Beej's Guide to Unix Interprocess Communication”
http://www.cs.cmu.edu/afs/cs/academic/class/15213-f00 “Network programming”
DPI
Standard:
IEEE Standard for SystemVerilog--Unified Hardware Design, Specification, and Verification Language (Annex H and Annex I )
Wiki:
https://en.wikipedia.org/wiki/SystemVerilog_DPI
Tutorial:
Book C.Spear, G.Tumbush “SystemVerilog for Verification”
SystemVerilog DPI Tutorial https://www.doulos.com/knowhow/sysverilog/tutorial/dpi/
Internet Resources
Notes: Free TCP/IP libraries or Socket libraries have a very good representation all over the internet. A simple google search points to thousands of links that contain open source and commercial libraries, tons of books, tutorials and forum discussions.
On the other hand, the number of resources dedicated to SV DPI is much smaller, but still, have a good representation all over the internet. The First of all, it is a SystemVerilog LRM. The next the most popular resources are conference papers, books and internet tutorials.

## Slide 6: Introduction
Socket interface for RTL simulation still exists as a proprietary application-specific solution.
Just a few basic TCP/IP SV DPI code examples available on the internet:
C. Spear. “Sockets, SystemVerilog http://spearzone.com/mb/systemverilog/examples/sockets_dpi.tar
SOLVNET ARTICLE: Modelling Multiple C Sockets Using SV-DPI
TCP+DPI
Notes: So, my expectation was to see at least some open source resources available on the internet.
However, I was able to find only a few basic examples. Even the Synopsys solvnet has almost nothing.
The lack of the open source resources was a motivation to create an open source dpi library.

## Slide 7: “TCP/IP Shunt” Library
Overview(Goals)
The TCP/IP Shunt is Open Source Client/Server TCP/IP socket based communication library for SystemVerilog simulation.
Portability: It supports all known SystemVerilog (SV) 2012 data types and data structures.
Simple API model: The Shunt provides a simple, consistent API.
Extensibility. The Shunt enables a platform to build high level abstraction applications.
Scalability and flexibility. The library facilitates the development of communication between multiple stand-alone SV simulations and/or external applications. (SV<->SV,C<->SV)
Notes: Library development has been started with two main goals in mind:
The first goal is to cover all SV types
The second one is to have a support SV to SV as well as C to SV

## Slide 8: “TCP/IP Shunt” Library
Structure
Client-Server (SC)
Primitive (PRIM)
Handshake API (HS)
The PRIM layer(basic data communication): TCP/IP socket initialization + elementary data exchange (singular variable ‎data types)
The CS layer (advance data communication): one-dimensional arrays + vectors +transaction header structures
The HS layer (dynamic data communication): transaction data structures + functions for one-dimensional dynamic arrays
API specification -- https://rawgit.com/xver/Shunt/master/doc/index.html
Notes: The library is using a layered approach. Users can build applications based on any layer of this abstraction
Briefly, layers are offering the following:
The PRIM layer (basic data communication): TCP/IP socket initialization + elementary data exchange
The CS layer (advance data communication): one-dimensional arrays + vectors +transaction header structures
The HS layer (dynamic data communication): transaction data structures + functions for one-dimensional dynamic arrays

## Slide 9: “TCP/IP Shunt” Library
PRIM
The PRIM layer(basic data communication): TCP/IP socket initialization + elementary data exchange
shunt_prim_init_target
shunt_prim_init_initiator
shunt_prim_send_byte
shunt_prim_recv_byte
TCP/IP
shunt_dpi_initiator_init
shunt_dpi_target_init
C functions
SV/DPI functions
C functions
SV/DPI functions
shunt_dpi_send_byte
shunt_dpi_recv_byte
Initiator
Target
TCP/IP Socket initialization
One byte transfer
Notes: The PRIM layer contains basic TCP/IP socket initialization, some generic functions, and the SV-to-C elementary data exchange. Its main purpose is enabling basic data communication. The layer contains methods to send and receive singular variable data types such as one byte, one int, one bit and so on. The PRIM operation doesn't require any memory allocation.
TCP/IP socket initialization:
The typical TCP/IP system consists of one Initiator and one or more Targets. To uniquely identify a data exchange session, both Initiator and Target use a combination of an IP address and a port number as a connection ID tag aka "Socket.
One byte transfer:
There are two functions for each data type Send and Recv.
Dpi functions from SV domains are importing ”C” function .
SV-SV ,C-SV

## Slide 10: “TCP/IP Shunt” Library
SC
The CS layer (advance data communication): one-dimensional arrays + vectors +transaction header structures
shunt_prim_init_target
shunt_prim_init_initiator
TCP/IP
shunt_dpi_initiator_init
shunt_dpi_target_init
C functions
SV/DPI functions
C functions
SV/DPI functions
Initiator
Target
TCP/IP Socket initialization
One-dimensional int array transfer
shunt_cs_send_intV
shunt_cs_recv_intV
shunt_dpi_send_intV
shunt_dpi_recv_intV
Notes: CS layer main purpose is enable fixed size one-dimensional array transfer. Fixed array size implies that both Initiator and Target should know transferred sized and data type before the start of the transfer.
Cs layer use the PRIM layer TCP/IP initialization.
As you notice Slides 9 and 10 are very similar.
From the user API point of view changes are:
function name
and new function argument - size
CS layer also has Send Recv methods to transfer header structure data type that can be used to create a protocol handshake.
The user application is responsible for the proper memory garbage collection

## Slide 11: “TCP/IP Shunt” Library
HS
The HS layer (dynamic data communication): transaction data structures + functions for one-dimensional dynamic arrays
{Dynamic Memory allocation is based on header receive context}
shunt_cs_send_header
shunt_cs_recv_header
TCP/IP
C functions
SV/DPI functions
C functions
SV/DPI functions
shunt_dpi_send_header
shunt_dpi_recv_header
Initiator
Target
TCP/IP Socket initialization
Transaction header transfer
shunt_api_send
shunt_api_recv
shunt_dpi_hs_send_byte
shunt_dpi_hs_recv_byte
Dynamic array of bytes transfer transfer
Notes: The HS layer SystemVerilog domain provides transaction data structures and functions that send and receive one-dimensional dynamic arrays (HS layer SV->C->(TCP/IP)->C->SV Dynamic array handshake).
HS layer methods can be applied both for simple and for more complex packet communication handshakes. Users can use the predefined header-data load or define their own transaction structure.
The user application is responsible for the proper memory garbage collection.

## Slide 12: User Application Example
Definition (System)
READ ACK or READ DATA
WRITE REQ/ADDR and WRITE DATA
Target
WRITE ACK
ACK_NOT_READY
Write Data
ACK_OK
ACK_NOT_ READY
Read Data
Initiator
READ REQ/ADDR
Shared Memory
DPI/TCP
TCP/DPI
SV Simulation(Initiator)
Simulation(Target) SV
The Target simulation has shared memory segment
Notes: The Shunt provides a set of functions and data structures that can be used to facilitate user-defined handshake development.
We will explain how to use Shunt library methods based on following example.
A shared memory handshake has three components: "TCP/IP socket initialization" followed by a series of "Write transactions" and/or "Read transaction"
For a Write transaction, the initiator starts a write handshake with a write request, then, it waits for the write acknowledge. The Target sends a WRITE ACK with ACK_OK or ACK_NOT_READY status back to the Initiator.
For a Read Transaction, the Initiator polls the Target simulation by sending a Read request If the Target response shows that data is ready, the Initiator waits for the Target to complete a transaction with READ ACK .The Target response can be ACK_OK or ACK_NOT_READY.

## Slide 13: User Application Example
Definition(protocol)
Transaction Type
(WRITE REQ)
Address
(byte)
Data Payload
(4 bytes)
Transaction Type
(READ REQ)
Address
(byte)
Transaction Type (WRITE ACK)
ACK_OK or ACK_NOT_READY
Transaction Type (READ ACK)
ACK_OK or ACK_NOT_READY
Data Payload
(4 bytes)
A data handshake :
packet header + data payload.
data payload size is fixed to 4 bytes
The Target simulation has shared memory segment
Shared Memory
DPI/TCP
TCP/DPI
SV Simulation(Initiator)
Simulation(Target) SV
Notes: A data request packet handshake consists of the packet header and data payload.
The packet data payload size is fixed to 4 bytes.
The packet header stores the following attributes:
Transaction types: read data (READ_REQ), write data (WRITE_REQ), read acknowledge (READ_ACK), and write acknowledge (WRITE_ACK)
Transaction address: Address is 8 bits.

## Slide 14: User Application Example
Common defines
Transaction Type
(WRITE REQ)
Address
(byte)
Data Payload
(4 bytes)
Transaction Type
(READ REQ)
Address
(byte)
Transaction Type (WRITE ACK)
ACK_OK or ACK_NOT_READY
Transaction Type (READ ACK)
ACK_OK or ACK_NOT_READY
Data Payload
(4 bytes)
A data handshake :
packet header + data payload.
data payload size is fixed to 4 bytes
TCP host address:
`define MY_HOST "localhost"
TCP port
`define MY_PORT 3450
`define Data_payload_size 4
Protocol:
typedef enum{
WRITE_REQ,
READ_REQ,
ADDR,
ACK_OK,
ACK_NOT_READY } transaction_type_e;
Notes: The Initiator and the Target must know prior to the simulation a designated TCP host address and port. Also, predefined protocol properties need to be communicated to both sites

## Slide 15: User Application Example
TCP/IP Socket Initialization
shunt_prim_init_target
shunt_prim_init_initiator
TCP/IP
shunt_dpi_initiator_init
shunt_dpi_target_init
C functions
SV/DPI functions
C functions
SV/DPI functions
Initiator
Target
TCP/IP Socket initialization
socket_id = shunt_dpi_initiator_init(`MY_PORT);
socket_id = shunt_dpi_target_init(`MY_PORT,` MY_HOST);
Notes: The Initiator creates a socket, assigns a specified TCP/IP port to it and waits for Target connect request. The Target creates a socket, assigns an Initiator’s Internet address-port pair, and creates a connection with the initiator. It takes only two simple function calls to establish a communication.

## Slide 16: User Application Example
Write Data
WRITE REQ/ADDR and WRITE DATA
Target
WRITE ACK
ACK_NOT_READY
Initiator
Transaction Type
(WRITE REQ)
Address
(byte)
Data Payload
(4 bytes)
Transaction Type (WRITE ACK)
ACK_OK or ACK_NOT_READY
typedef struct {
real trnx_type;//shunt_dpi_hash(“WRITE_REQ”)or shunt_dpi_hash(“ACK_OK”);
real trnx_id; //Transaction ID (N/A)
real data_type;//shunt_dpi_hash (“SHUNT_BYTE”)or shunt_dpi_hash(“SHUNT_HEADER_ONLY”)
int n_payloads;//Data_payload_size = 4
} cs_header_t;
Initiator:
shunt_dpi_send_header(socket_id,write_req)
shunt_dpi_send_byte(socket_id,ADDR)
shunt_dpi_hs_send_byte(sockid,write_req,Data)
shunt_dpi_recv_header (socket_id,ack);
Target:
shunt_dpi_recv_header(socket_id,write_req)
shunt_dpi_recv_byte(socket_id,ADDR)
{memory allocation} shunt_dpi_hs_recv_byte(socket_id,data_ack,Data)
shunt_dpi_send_header(socket_id,ack);
Notes: The Shunt library has predefined header structure (cs_header_t) and corresponding send/receive methods that can be applied to produce a protocol request-acknowledge pair

## Slide 17: User Application Example
Read Data
typedef struct {
real trnx_type;//shunt_dpi_hash(“READ_REQ”)or shunt_dpi_hash(“ACK_OK”);
real trnx_id; //Transaction ID (N/A)
real data_type;//shunt_dpi_hash (“SHUNT_BYTE”)or shunt_dpi_hash(“SHUNT_HEADER_ONLY”)
int n_payloads;//Data Payload size = 4
} cs_header_t;
Initiator:
shunt_dpi_send_header(socket_id,read_req)
shunt_dpi_send_byte(socket_id,ADDR)
shunt_dpi_recv_header(socket_id,read_ack)
{memory allocation}
shunt_dpi_hs_recv_byte(sockid,read_req,Data)
Target:
shunt_dpi_recv_header(socket_id,read_req)
shunt_dpi_recv_byte(socket_id,ADDR)
shunt_dpi_send_header(socket_id,read_ack); shunt_dpi_hs_send_byte(socket_id,read_ack,Data)
Target
ACK_NOT_ READY
Initiator
READ REQ/ADDR
READ ACK or READ DATA
Transaction Type
(READ REQ)
Address
(byte)
Transaction Type (READ ACK)
ACK_OK or ACK_NOT_READY
Data Payload
(4 bytes)

## Slide 18: Summary
import shunt_dpi_pkg::*;
SystemVerilog DPI "TCP/IP Shunt" (TCP/IP SystemVerilog socket library) https://github.com/xver/Shunt
"TCP/IP Shunt API specification” https://rawgit.com/xver/Shunt/master/doc/index.html
The Shunt is available under a MIT License. It can be used without restriction in an open-source or commercial application

## Slide 20: Backup
Subtitle if Needed

## Slide 21: SV data types
typedef enum {
    SHUNT_INT,
    SHUNT_REAL,SHUNT_SHORTREAL,
    SHUNT_STRING,
    SHUNT_A_STRUCTURE,
    SHUNT_INTEGER,
    SHUNT_BYTE,
    SHUNT_REG,
    SHUNT_BIT,
    SHUNT_SHORTINT,
    SHUNT_LONGINT,
    SHUNT_HEADER_ONLY
} SHUNT_INSTR_ENUM
Integer 2 states:
  SHUNT_INT- SV type int
  SHUNT_SHORTINT- SV type shortint
  SHUNT_LONGINT- SV type longint
  SHUNT_BYTE- SV type byte
  SHUNT_BIT- SV type bit
Integer 4 states:
  SHUNT_INTEGER- SV type integer, time
  SHUNT_REG- SV type reg, logic
Non integer types IEEE 754:
  SHUNT_REAL- SV type real, realtime
  SHUNT_SHORTREAL- SV type shortreal
Special
  SHUNT_STRING- SV type string
  SHUNT_A_STRUCTURE - complex data types/user defined data types: arrays/struct,union,enums
  SHUNT_HEADER_ONLY- Shunt type cs_header_t header only.

## Slide 22
Fringe Initialization
TCP connection
Endpoint Registration

## Slide 23: Fringe PnP
Initiator
Target
Step1:Fringe Initialization
Step 2 TCP connection
FRNG_REG_REQ
FRNG_REG_ACK
socket_id;
child socket_id
Step 3 Registration
h_.trnx_type = shunt_dpi_hash("FRNG_REQ");
h_.data_type = shunt_dpi_hash(who_iam());
h_.trnx_id = 0;
h_.n_payloads = sim_id;
If (OK)
SrcDsts_db[Target].socket_id = child socket_id;
SrcDsts_db[Target].status = FRNG_SRCDST_ACTIVE;
h_.trnx_type = shunt_dpi_hash("FRNG_ACK");
h_.data_type = shunt_dpi_hash(Target name);
IF(OK) h_.trnx_id = SrcDsts_db[Target].SrcDst_id
IF(ERR) h_.trnx_id = -1 ; //ACK ERROR
h_.n_payloads = sim_id;
SrcDsts_db[Initiator].socket_id = socket_id;
SrcDsts_db[Target].socket_id = socket_id;
If (OK) SrcDsts_db[Target].status = FRNG_SRCDST_ACTIVE;
If (OK) SrcDsts_db[Initiator].status = FRNG_SRCDST_ACTIVE;

## Slide 25
FRNG_REG_REQ
Initiator
Target
Step1:Fringe Initialization
h_.trnx_type = shunt_dpi_hash("FRNG_REQ");
h_.data_type = shunt_dpi_hash(who_iam());
h_.trnx_id = 0;
h_.n_payloads = sim_id;
If (OK)
SrcDsts_db[Target].socket_id = child socket_id;
SrcDsts_db[Target].status = FRNG_SRCDST_ACTIVE;
FRNG_REG_ACK
Step 2 TCP connection
socket_id;
child socket_id
h_.trnx_type = shunt_dpi_hash("FRNG_ACK");
h_.data_type = shunt_dpi_hash(Target name);
IF(OK) h_.trnx_id = SrcDsts_db[Target].SrcDst_id
IF(ERR) h_.trnx_id = -1 ; //ACK ERROR
h_.n_payloads = sim_id;
SrcDsts_db[Initiator].socket_id = socket_id;
SrcDsts_db[Target].socket_id = socket_id;
If (OK) SrcDsts_db[Target].status = FRNG_SRCDST_ACTIVE;
If (OK) SrcDsts_db[INITIATOR].status = FRNG_SRCDST_ACTIVE;
Step 3 Registration

## Slide 26: Fringe Put
h_.trnx_type = shunt_dpi_hash("FRNG_PUT");
h_.data_type = signals_db[signals_db_index].data_type;
h_.trnx_id = signals_db[signals_db_index].signal_id;
h_.n_payloads = signals_db[signals_db_index].signal_size;
FRNG_REG_REQ
PnP Agent 1
PnP Agent 2
FRNG_REG_ACK
h_.trnx_type = shunt_dpi_hash("FRNG_ACK");
h_.data_type = shunt_dpi_hash(Target name);
IF(OK) h_.trnx_id = SrcDsts_db[Target].SrcDst_id
IF(ERR) h_.trnx_id = -1 ; //ACK ERROR
h_.n_payloads = sim_id;
SrcDsts_db[Initiator].socket_id = socket_id;
SrcDsts_db[Target].socket_id = socket_id;
If (OK) SrcDsts_db[Target].status = FRNG_SRCDST_ACTIVE;
If (OK) SrcDsts_db[Initiator].status = FRNG_SRCDST_ACTIVE;

## Slide 27: “TCP/IP Shunt” Library
PRIM
The PRIM layer(basic data communication): TCP/IP socket initialization + elementary data exchange
shunt_prim_init_target
shunt_prim_init_initiator
shunt_prim_send_byte
shunt_prim_recv_byte
TCP/IP
shunt_dpi_initiator_init
shunt_dpi_target_init
Fringe functions
RTL
Fringe functions
RTL
shunt_dpi_send_byte
shunt_dpi_recv_byte
PnP Agent 1
PnP Agent2
TCP/IP Socket initialization
One byte transfer
Notes: The PRIM layer contains basic TCP/IP socket initialization, some generic functions, and the SV-to-C elementary data exchange. Its main purpose is enabling basic data communication. The layer contains methods to send and receive singular variable data types such as one byte, one int, one bit and so on. The PRIM operation doesn't require any memory allocation.
TCP/IP socket initialization:
The typical TCP/IP system consists of one Initiator and one or more Targets. To uniquely identify a data exchange session, both Initiator and Target use a combination of an IP address and a port number as a connection ID tag aka "Socket.
One byte transfer:
There are two functions for each data type Send and Recv.
Dpi functions from SV domains are importing ”C” function .
SV-SV ,C-SV

## Slide 28
Fringe PUT(input Destination,input Signal)
Fringe GET
Get
RTL
Signal DB entry:

## Slide 29
PUT
Send
TCP
SrcDsts_db[indx].signal_status
FRNG_SIGNAL_VALID_PUT
signals_db[indx].signal_valid FRNG_SIGNAL_VALID_PUT
signals_db_payloads
FRNG_SIGNAL_VALID_PUT
API Thread
DB thread

## Slide 30: Fringe Put
RTL thread
signals_db[i].signal_valid == FRNG_SIGNAL_IDLE
fringe_api_put(dst,signal,type,data)
Set by RTL: signals_db_payloads[index_payloads+i]=data
Set by RTL: signal_valid=FRNG_SIGNAL_VALID_PUT
If
signals_db[i].
If
signals_db[i].signal_valid == FRNG_VALID_PUT
fringe_put(dst,signal,type,data)
Send data to
External TCP endpoint
Set by Fringe: signal_valid=FRNG_SIGNAL_IDLE
Fringe thread

## Slide 31: Fringe Get
RTL thread
signals_db[i].signal_valid == FRNG_SIGNAL_GET
fringe_api_get(src,signal,type,data)
Set by Fringe: signals_db_payloads[index_payloads+i]=data
Set by Fringe: signal_valid=FRNG_SIGNAL_GET
If
signals_db[i].
If
signals_db[i].signal_valid == FRNG_SINAL_IDLE
fringe_get(dst,signal,type,data)
Get data from
External TCP endpoint
Set by RTL: signal_valid=FRNG_SIGNAL_IDLE
Fringe thread

## Slide 32
Fringe
Fringe
Source EP RTL
Destination EP RTL
fringe_api_put(dst,signal,type,data)
fringe_api_get(src,signal,type,data)
TCP/IP

## Slide 33
Fringe DB
Fringe DB
Front-End API thread
Front-End API thread
fringe_api_put(dst,signal,type,data)
fringe_api_get(src,signal,type,data)
TCP/IP
Back-End API thread
Back-End API thread
Source
Destination

## Slide 34
Fringe DB
Fringe DB
fringe_api_put(dst,signal,type,data)
fringe_api_get(src,signal,type,data)
TCP/IP
fringe_api_get(src,signal,type,data)
fringe_api_put(dst,signal,type,data)